## Slide 1: Using Geology to Communicate Radon Potential to the Public
Bethany Overfield, M.S., William Andrews Jr., Ph.D.
University of Kentucky, Kentucky Geological Survey
Lexington, KY
Amanda Wiggins, Ph.D., Ellen J. Hahn, Ph.D., Renee Fox, M.S.
University of Kentucky College of Nursing, BREATHE
Lexington, KY

## Slide 2
Collaboration between Kentucky Geological Survey and UK College of Nursing
The geology of radon
Creation of Radon Potential Maps
Role of geology in assessing radon potential
Future work
Outline

## Slide 3
BREATHE
Bridging Research Efforts and Advocacy Toward Healthy Environments (BREATHE) is a multidisciplinary research, outreach, and practice collaborative of the UK College of Nursing with partners internal and external to UK.
Mission: is to promote lung health and healthy environments to achieve health equity.
Kentucky Geological Survey (KGS)
The Kentucky Geological Survey is a state supported research center and public resource within the University of Kentucky.
Mission: conduct research and provide unbiased information about geologic resources, environmental issues, and natural hazards affecting Kentucky.

## Slide 4
County-based radon map inspired the collaboration between KGS and BREATHE.
Radon data obtained by BREATHE researchers were analyzed by county and zip code; political boundaries are not, however, optimal for describing the extent of physical phenomena.
Radon levels have the potential to vary within a county, based on the context of geology.

## Slide 5
Kentucky leads the nation in the incidence of new lung cancer cases and lung cancer mortality.
Radon is the second leading cause of lung cancer.
Those exposed to both radon and tobacco smoke are 10 times more likely to develop lung cancer.
Kentucky has high radon potential (because of the geology), high smoking rates, and weak smoke-free protections.

## Slide 6
Breakdown of Uranium--------> Radium--------> Radon--------> Polonium--------> Lead
All rocks contain some uranium
Rocks with high Uranium: light colored volcanics, granites, dark shales, sedimentary rocks that contain phosphates, and metamorphic rocks derived from these rocks.
Parent material
Daughter materials
Otton, James, 1992, The Geology of Radon, USGS General Interest pub

## Slide 7
Radium--------> Radon
Radium decays by ejecting an alpha particle (composed of two neutrons and two protons)
As the alpha particle is ejected, the newly formed radon atom recoils and is shot off in the opposite direction!
Alpha recoil most important factor affecting the release of radon from mineral grains in a rock or soil.
Otton, James, 1992, The Geology of Radon, USGS General Interest pub

## Slide 8
Mineral grains in a rock or soil:
Radon atom can be shot from a mineral grain into:
• the same mineral grain
• another mineral grain
• pore space
• water in pore space
Radon that enters pore space becomes available to movement.
Otton, James, 1992, The Geology of Radon, USGS General Interest pub

## Slide 9
Radon movement
Otton, James, 1992, The Geology of Radon, USGS General Interest pub
Radon is a gas, which makes it more mobile
It travels through fractures and openings in rock or through pore space
The method and speed of radon movement through rock/soil is controlled by water in the pore space, the % of pore space, and the permeability of rock/soil (“interconnectedness”)

## Slide 10
Radon movement
Otton, James, 1992, The Geology of Radon, USGS General Interest pub
Radon can enter a home through many paths
Groundwater often overlooked as a pathway

## Slide 11
Kentucky has different rock types underneath the surface. Some rocks have the potential to release more radon gas than others based on the amount of uranium in them.

## Slide 12
Geologic Mapping in Kentucky
The near-surface bedrock geology is mapped at a very detailed scale (1:24,000, 1 inch = 2000 ft.)

## Slide 13
Each map color represents a different geologic unit called a geologic formation
Geologic formations are made up of rock types (e.g. sandstone, limestone, shale)
Rock types have different radon potential depending on the minerals present
In Kentucky radon producing rocks:
• dark shale • high phosphate sedimentary rocks (limestone) Rocks can serve as a source of radon and as a pathway for radon
Geologic Mapping in Kentucky

## Slide 14
BREATHE team acquired 60K+ residential radon test data points (short term test results)
Addresses converted to lat/long coordinates; duplicates eliminated

## Slide 15
60K+ data point locations intersected with geology
Geologic formation assigned a radon value based on data points within the formation
Example data set:

## Slide 16
Created a statewide radon potential map
Much more detailed than county-level maps
Show considerable variation within counties

## Slide 17
Christian County
Edmonson County
EPA county-level maps
KGS geology-based maps

## Slide 18
Produced 120 county-based infographics for general public

## Slide 19
Current maps available on the web by county.

## Slide 20
We wanted an interactive way for folks to look at the data that could easily be updated:
Kentucky Radon Potential online mapping service

## Slide 21
Using the “information (i)” icon, a dialog box is returned with data.
The first page links to the static county infographic

## Slide 22
The second page of the dialog box offers information about geology, the number of radon test results in the geologic formation, along with the min, max, and q3 values.

## Slide 23
Do KY limestones have different chemical compositions (levels of Uranium) or is high radon in MS limestones due to fractures\karst topography? Or both?
Important questions about geologic control on radon source in Kentucky:

## Slide 24
Validate radon potential maps with new data
-Acquire equipment to take soil-gas samples to verify the county maps
Assess radon in groundwater
Make the online Kentucky Radon Potential mapping service more robust and interactive.
Continue making radon potential maps using new data sources.
-long term tests vs. short term tests ( WE CAN ALWAYS USE MORE DATA!)
Research with existing 60K residential radon data set:
-Climate/seasonal influence on radon gas migration
Life cycle of radon as it pertains to geologic units:
-sample geologic units to assess major, minor, and trace elements using x-ray fluorescence
Radon potential maps based on geology are a great starting point, but data set has obvious limitations (lateral variation in a geologic unit, structure of home, residential testing issues).
Future Work

## Slide 25
Questions?